## Slide 1
Ramos Wang · SID 550378666
Supervisor: Prof. Yonghui Li
ELEC5223 Dissertation B · School of Electrical and Computer Engineering
The University of Sydney
Final defence
Text-Guided Segmentation of COVID-19 Infections
in Chest X-rays
Notes: English speaker notes
This work studies FSDR and complete RACE for text-guided infection segmentation in chest X-rays. All headline results use the fixed Test split and the matched single-cycle cosine study.
中文讲稿
本次汇报介绍 FSDR 和完整 RACE 胸片感染分割。主结论来自固定测试集，以及采用单次余弦的匹配实验。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 2
Text-guided infection segmentation
QaTa-COV19 v2 · example C07 · dataset-provided description
2
Chest X-ray
Report
“Bilateral pulmonary infection,
two infected areas, upper left
lung and lower right lung.”
Ground-truth mask
+
Semantic cues are coarse
Fusion must retain local spatial detail.
Report and image may disagree
Routing should also use visual evidence.
Notes: English speaker notes
The input is a chest X-ray and its dataset-provided text description, and the target is a binary infection mask. This is the exact description paired with C07. Anatomical wording is preserved as supplied; it is not a new clinical interpretation. The design motivations are detail-preserving fusion and report-image agreement.
中文讲稿
输入为胸片和数据集配套描述，输出感染二值掩膜。展示的是 C07 原始配对描述，保留数据集解剖措辞，不重新进行临床判断。设计动机是兼顾语义与细节，并在报告引导中引入视觉一致性。
Sources
evidence/case_reports.json
assets/C07_image.png
assets/C07_gt.png
evidence/qualitative_selection.json

## Slide 3
Two architectural contributions
Matched single-cycle cosine · three seeds · Test macro IoU
3
FSDR
Frequency-aware Semantic–Detail Refinement
Keep CNN, ViT and decoder features separate during refinement.
Use semantic support to guide local detail.
+0.51 pp
vs. matched PLAM
RACE
Report–Anatomy Consistency and Evidence Fusion
Gate CNN skips with a report prior and visual evidence.
Evaluate routing and auxiliary training as one complete module.
+0.24 pp
added to FSDR
Notes: English speaker notes
FSDR changes decoder skip fusion. Complete RACE refines CNN skips using report, anatomy and visual evidence and includes auxiliary training. The gains are 0.5058 and 0.2428 percentage points, respectively. Auxiliary supervision is not claimed as a separate innovation.
中文讲稿
FSDR 改变解码器跳跃融合。完整 RACE 利用报告、解剖与视觉证据精炼 CNN 跳连，并包含辅助训练。两项增益分别为 0.5058 和 0.2428 个百分点，不将辅助监督单独计为创新点。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 4
FSDR and RACE within LViT
Same labels identify matching feature ports · T: frozen CXR-BERT features · B: anatomical basis
4
ViT branch
CNN encoder
Skip refinement
CNN decoder
Report → CXR-BERT → T
X-ray ↓
↑ Mask
Down 1
Up 1
C1
RACE 1
FSDR 1
C1, T
V1
T, B
up1: V1, T
C′1
Down 2
Up 2
C2
RACE 2
FSDR 2
C2, T
V2
T, B
up2: V2, T
C′2
Down 3
Up 3
C3
RACE 3
FSDR 3
C3, T
V3
T, B
up3: V3, T
C′3
Down 4
Up 4
C4
RACE 4
FSDR 4
C4, T
V4
T, B
up4: V4, T
C′4
C5 · Bottleneck
Notes: English speaker notes
The double-U structure follows LViT. CNN features enter the same-scale ViT stages, and reconstructed ViT features V1–V4 return to the decoder. RACE refines only the decoder-bound CNN skips; the CNN encoder continues with the original features. FSDR is inside each up stage and replaces PLAM fusion. The labelled ViT, text and anatomy ports avoid crossing wires. Adaptive filtering is active only at up4 and up3.
中文讲稿
整体保留 LViT 双 U 结构。同尺度 CNN 特征进入 ViT，重建 ViT 特征 V1–V4 返回解码器。RACE 仅精炼发往解码器的 CNN 跳连，编码器主路径继续使用原特征。FSDR 位于每个 up stage 内，替换 PLAM 融合。图中以同名端口连接 ViT、文本和解剖条件，自适应滤波仅作用于 up4/up3。
Sources
nets/LViT.py
nets/eppa.py
nets/race_fuse.py
docs/presentations/20260922/drawio/FSDR_RACE_architecture_concise.drawio

## Slide 5
PLAM and FSDR fusion paths
C*: C with FSDR alone; C′ after RACE in the combined model · D: upsampled decoder feature
5
PLAM
C
V
+
PLAM
D
Concat
3×3 ×2
CNN and ViT are added before pixel weighting.
FSDR
C*
V
D
FSDR
Y
D′
Concat
3×3 ×2
T
Distinct sources remain available for refinement.
Notes: English speaker notes
PLAM receives the sum of CNN and reconstructed ViT features. FSDR keeps CNN, ViT, decoder and text features separate while computing corrections. It outputs a refined skip Y and decoder D prime before concatenation and two convolutions. D prime equals D at shallow stages. The matched baseline uses our common recipe, not an unchanged reproduction of the official training pipeline.
中文讲稿
PLAM 接收 CNN 与 ViT 重建特征之和。FSDR 在计算修正时保留 CNN、ViT、解码器和文本来源，输出 Y 与 D′ 后再拼接并卷积。浅层 D′=D。匹配基线使用本研究共同配方，不等同于官方完整训练流程原样复现。
Sources
nets/LViT.py
nets/eppa.py
docs/results/plam_baseline_audit_20260916/AUDIT.md

## Slide 6
FSDR: semantic support guides detail
One scale shown · adaptive filtering at up4/up3 is detailed in the backup slides
6
C*
Haar
Low
High
Channel
gate
Text FiLM
Region support
Semantic
fusion
Local + dilated
Conv
Detail
fusion
+
Y
Vlow, D′low, T
Vlow
S
Identity
Y = C* + Rsem + αd Rdetail + Radapt
Rsem: channel, region and ViT residuals · Radapt and D′: adaptive branch → backup
Notes: English speaker notes
This schematic isolates the semantic-detail paths. Fixed Haar decomposition separates low and high frequencies. Low-frequency CNN, ViT and refined decoder context plus text produce semantic corrections and region support S. S guides high-frequency local and dilated convolution refinement. The original CNN feature bypass is retained. The equation also includes the adaptive residual, whose bank and decoder update appear in the backup. Dashed context ports are schematic; this is not a proof that each mechanism alone causes the measured gain.
中文讲稿
本页突出语义与细节两条路径：Haar 固定分频，低频 CNN、ViT、精炼解码器及文本产生语义修正与区域支持 S；S 引导高频局部/扩张卷积精炼。保留原始 CNN 特征恒等路径。公式中的自适应残差和 D′ 见备份。该图说明设计，不将各内部机制单独宣称为已验证的增益来源。
Sources
nets/eppa.py
docs/FSDR.md

## Slide 7
RACE: prior, evidence and agreement
C1–C4 skips · bounded residual update · auxiliary objectives are used during training
7
Report prior
T
Masked mean
Slot MLP
z
B · 6 zones
Prior P
σ
Visual evidence
C
Conv ×2 → σ
Evidence E
Zone pool
Agreement A
P × E × A
Gate G
B
z
q
A
E
C′ = C + s G ⊙ R(C)
R(C): DWConv → PWConv
s = 0.15 tanh(a), initially zero
Notes: English speaker notes
Text features are pooled and mapped to six slot logits and probabilities z. The anatomical basis B maps those values to a spatial prior P. CNN features yield visual evidence E; anatomical zone pooling gives q, compared with z to obtain an agreement scalar A. Their product is G. A bounded, initially zero residual scale preserves the identity path. GroupNorm and GELU are omitted from the diagram for clarity and remain in the code. Count and slot auxiliary objectives belong to training; ground truth is not used in inference. Complete RACE is what the three-seed experiment measures.
中文讲稿
文本经过池化与槽位预测得到 z，再与六区域解剖基底 B 形成空间先验 P。CNN 产生视觉证据 E，经区域池化得到 q，与 z 比较得到一致性标量 A。三者相乘为 G，以初始为零的有界残差尺度修正 C。图中为易读省略 GN/GELU，代码保留。计数及槽位辅助目标用于训练，推理无需 GT。三种子实验评价完整 RACE。
Sources
nets/race_fuse.py
nets/LViT.py

## Slide 8
Matched experimental design
Primary comparison · all 12 runs completed · single-cycle cosine
8
Item | Shared protocol
Data | QaTa-COV19 v2 · Train 5,716 / Val 1,429 / Test 2,113
Input / text | 224 × 224 · frozen CXR-BERT · 32 tokens · no LoRA
Optimisation | 80 epochs · batch 16 · Adam · weight decay 10⁻⁴
Learning rate / loss | Single-cycle cosine: 3×10⁻⁴ → 10⁻⁶ · Dice + Focal
Comparison | PLAM / FSDR × RACE off / on · seeds 1219, 2027, 3407
Selection / metric | Best Val macro IoU · Test macro IoU / Dice · probability > 0.5
Hold the recipe fixed; change the architectural modules.
Test has prior research access. Split-audit limitations are retained in the backup.
Notes: English speaker notes
The primary evidence uses a two-by-two architecture ablation across three seeds under one fixed protocol. Dice and Focal weights are 0.5 each, with focal gamma 2. The best checkpoint is selected only by validation macro IoU, then evaluated with a fixed strict threshold. The evaluation is retrospective, not an untouched prospective Test study.
中文讲稿
核心证据为固定配方下两因素四配置、三种子的消融。Dice/Focal 权重均为 0.5，gamma=2。以验证集 macro IoU 选 Best，固定严格 >0.5 阈值后评估 Test。测试集曾用于研究，属于回顾性评价。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 9
Test results across three seeds
Mean ± sample SD · macro metrics · percentage-point gain over matched PLAM
9
Configuration | Test IoU (%) | Test Dice (%) | Δ IoU (pp)
Matched PLAM | 75.48 ± 0.09 | 84.03 ± 0.08 | —
FSDR | 75.98 ± 0.15 | 84.50 ± 0.08 | +0.51
PLAM + complete RACE | 75.70 ± 0.11 | 84.19 ± 0.07 | +0.22
FSDR + complete RACE | 76.23 ± 0.05 | 84.71 ± 0.03 | +0.75
76.23%
Test IoU
+0.75 pp
over matched PLAM
Notes: English speaker notes
The combined model reaches 76.2262 plus or minus 0.0456 percent Test IoU and 84.7112 plus or minus 0.0348 percent Dice. Relative to matched PLAM the gains are 0.7487 and 0.6861 percentage points. Display rounding is two decimals, while every raw run is kept in the backup and source JSON. RACE means the complete module including auxiliary training.
中文讲稿
组合 Test IoU 为 76.2262±0.0456%，Dice 为 84.7112±0.0348%；相对匹配 PLAM 分别提高 0.7487 和 0.6861 个百分点。主表仅显示两位小数，全部原始运行与更高精度保留在备份和 JSON。RACE 指包含辅助训练的完整模块。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 10
Positive IoU gains in every paired seed
Same-seed contrasts · Test macro IoU gain in percentage points
10
Chart: 
| FSDR − PLAM | Complete RACE added to FSDR | Combined − PLAM
Seed 1219 | 0.24233 | 0.43871 | 0.68104
Seed 2027 | 0.61909 | 0.17039 | 0.78948
Seed 3407 | 0.65607 | 0.11941 | 0.77549
Combined gain: +0.68 to +0.79 pp across the three seeds.
Three positive repetitions support consistency under this recipe; they do not establish universal stability.
Notes: English speaker notes
Every displayed same-seed gain is positive. The combined improvement spans 0.6810 to 0.7895 percentage points. The full five-contrast table appears at the end of the backup. Three seeds support consistency in this protocol but are not evidence of universal stability or a population-level significance claim. Embedded chart values are rounded to six decimals for Excel portability, and visible labels to two; the unrounded source JSON is retained.
中文讲稿
图中三种配对比较的全部种子增益为正，组合提升范围 0.6810–0.7895 个百分点。完整五组对比放在备份末页。三次重复支持本配方下的一致性，不宣称普遍稳定或总体统计显著。内嵌图表数值保留六位小数以兼容 Excel，标签显示两位，原始 JSON 保留完整精度。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 11
External methods on the same Test images
Context comparison · 2,113 images · fixed probability > 0.5 · training recipes differ
11
Method | Model source | IoU (%) | Dice (%)
MMI-UNet | Author checkpoint | 75.48 | 83.97
GuideDecoder | Retrained · seed 1219 | 75.29 | 83.88
DD-CMD | Retrained · seed 1219 | 76.30 | 84.75
FSDR + complete RACE | Three-seed mean | 76.23 | 84.71
The matched module ablation is the core evidence for the contributions.
DD-CMD remains slightly higher (+0.0732 pp IoU). This comparison does not support a SOTA claim.
Notes: English speaker notes
External methods are evaluated on the same 2113 Test images at the same threshold. MMI uses the author checkpoint; GuideDecoder and DD-CMD are single-seed retrainings with their own recipes. Our row averages three models. DD-CMD is 0.0732 IoU percentage points higher. This is contextual evidence, while the recipe-matched ablation isolates our module changes.
中文讲稿
外部方法采用相同 2113 张 Test 与相同阈值。MMI 使用作者权重，GuideDecoder/DD-CMD 为各自配方的单种子复训，本方法为三种子均值。DD-CMD 高 0.0732 个 IoU 百分点。此表提供背景，模块增益以同配方消融为核心证据。
Sources
evidence/external_results.json
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json
docs/results/text_guided_baselines_20260920/FINAL_REPORT.md

## Slide 12
C07: reduced missed regions
Selected qualitative example · J0/J2: seed 3407 · J1/J3: seed 2027 · not a paired-seed ablation
12
Chest X-ray
Ground truth
Matched PLAM
FSDR + RACE
IoU 44.68%
IoU 82.16%
TP
FP
FN
Less missed infection in the highlighted region.
Same region
Detail view
Notes: English speaker notes
C07 illustrates reduced false-negative area relative to the selected PLAM checkpoint. The main row shows each image once rather than duplicating masks and errors. Zooms show the same image coordinates. These selected checkpoints use different seeds, so this slide illustrates a case and does not attribute the full per-image gain causally to one module.
中文讲稿
C07 展示相对所选 PLAM 模型漏分区域减少。主排不再重复展示二值掩膜和误差图，局部放大保持相同坐标。使用不同种子的模型，只作定性说明，不能将该图全部增益归因于单一模块。
Sources
evidence/qualitative_selection.json
evidence/qualitative_metrics.csv
assets/C07_comparison.png

## Slide 13
G18: a remaining boundary error
Selected qualitative example · J0/J2: seed 3407 · J1/J3: seed 2027 · not a paired-seed ablation
13
Chest X-ray
Ground truth
PLAM + RACE
FSDR + RACE
IoU 81.29%
IoU 78.30%
TP
FP
FN
The combined model still oversegments the boundary.
Same region
Detail view
Notes: English speaker notes
G18 is retained as a limitation: the combined model scores 78.3001 percent IoU versus 81.2922 for PLAM plus RACE, a decrease of 2.9921 percentage points. Boundary false positives remain. The selected checkpoints use different seeds; this is a qualitative limitation, not a matched causal estimate.
中文讲稿
保留 G18 的局限：组合 IoU 为 78.3001%，低于 PLAM+RACE 的 81.2922%，下降 2.9921 个百分点，仍有边界误分。这是跨种子定性局限，不是匹配因果估计。
Sources
evidence/qualitative_selection.json
evidence/qualitative_metrics.csv
assets/G18_comparison.png

## Slide 14
Conclusions
Primary evidence: four configurations × three seeds · Test macro metrics
14
FSDR preserves source-specific information during fusion.
+0.51 pp mean IoU over matched PLAM.
Complete RACE adds report–image agreement to skip refinement.
+0.24 pp when added to FSDR; routing alone needs repeated controls.
76.23% Test IoU · 84.71% Dice
+0.75 pp IoU over matched PLAM, with a positive gain in every seed.
Next: independent-cohort evaluation and repeated routing-versus-auxiliary controls.
Notes: English speaker notes
The strongest supported claim is the matched three-seed improvement of FSDR and complete RACE on this dataset and protocol. The combined model improves mean Test IoU by 0.7487 percentage points. Remaining limits include retrospective Test access, split independence, and a single-seed routing-versus-auxiliary diagnosis. Independent-cohort evaluation and repeated mechanism controls are the next evidence needed.
中文讲稿
最强结论是在当前数据集与配方下，三种子匹配实验支持 FSDR 与完整 RACE，组合平均 Test IoU 提高 0.7487 个百分点。限制包括测试集的既往研究使用、数据划分独立性，以及路由/辅助训练诊断仅有单种子。后续需独立队列与重复机制对照。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 15
Thank you
Questions welcome. Backup material follows.
Ruoheng (Ramos) Wang · ELEC5223 Dissertation B · Supervisor: Prof. Yonghui Li
Notes: English speaker script
Thank you. I welcome questions about the two modules, the matched ablations and the interpretation of the completed results.
中文讲稿
谢谢。欢迎就两个模块、匹配消融及最终结果的解释提问。
Sources · 15 September 2026

## Slide 16
Backup slides
Results, formulation, protocol and supporting evidence
Notes: English speaker script
The backup slides contain detailed fusion results, the FSDR formulation, the separate learning-rate study, fixed-model RACE diagnostics, evaluation protocol and report-target binding comparisons.
中文讲稿
备用页提供详细融合成绩、FSDR 公式、独立学习率实验、RACE 固定模型诊断、评估协议及报告目标绑定对照。
Sources · 15 September 2026

## Slide 17
All primary runs: Test results
Backup: all 12 primary models
17
Configuration | Seed | Best epoch | Test IoU (%) | Test Dice (%)
LViT-PLAM | 1219 | 61 | 75.5675 | 84.0604
LViT-PLAM | 2027 | 72 | 75.4668 | 84.0771
LViT-PLAM | 3407 | 74 | 75.3983 | 83.9379
FSDR only | 1219 | 67 | 75.8098 | 84.4236
FSDR only | 2027 | 68 | 76.0859 | 84.5739
FSDR only | 3407 | 75 | 76.0544 | 84.5117
PLAM + complete RACE | 1219 | 78 | 75.8189 | 84.2712
PLAM + complete RACE | 2027 | 72 | 75.6458 | 84.1648
PLAM + complete RACE | 3407 | 66 | 75.6239 | 84.1425
FSDR + complete RACE | 1219 | 75 | 76.2485 | 84.7097
FSDR + complete RACE | 2027 | 78 | 76.2562 | 84.7468
FSDR + complete RACE | 3407 | 70 | 76.1738 | 84.6773
Each run selects Best by Val macro IoU. Every configuration uses all three seeds.
Notes: English speaker script
This table retains all 12 primary results, including the weaker runs. The combined model achieves IoU values of 76.2485, 76.2562 and 76.1738 percent. Each Best epoch comes from validation selection. We report the mean over every seed rather than choosing a winning seed for the quantitative headline.
中文讲稿
本页保留全部十二个主实验模型，包括较弱种子。组合模型三个 IoU 为 76.2485%、76.2562%、76.1738%。Best 轮次均由验证集选择，量化主结论使用全部种子均值，不挑选最优种子作为成绩。
Sources (snapshot: 22 September 2026)
docs/results/stage1_overall_20260915/FINAL_REPORT.md
docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 18
FSDR: adaptive frequency refinement
Backup · up4 / up3 only · at up2 / up1: D′ = D and Radapt = 0
18
Clow, Vlow, Dlow
Context fusion
Conv → Softmax
wlow
Conv → Softmax
whigh
D
C*
Filter bank
LPlow(D)
Filter bank
LPhigh(C*)
D′ = D + α [LPlow(D) − D]
Radapt = β [C* − LPhigh(C*)]
Each bank mixes identity, 3×3 blur and 5×5 blur with spatially varying weights.
Notes: English speaker notes
The low-pass and high-pass branches learn different spatial mixing weights over the same three low-pass operators: identity, blur 3 and blur 5. The high-pass branch subtracts its learned low-pass result from the raw CNN skip. The decoder is updated by a bounded low-pass correction. Corrected D prime is Haar-split again before semantic refinement.
中文讲稿
低通与高通分支对恒等、3×3 模糊、5×5 模糊学习不同空间混合权重。高通分支由原始 CNN 跳跃特征减去其低通结果得到；解码器采用有界低通修正。D′ 随后重新做 Haar 分解进入语义精炼。
Sources
nets/eppa.py
docs/FSDR.md

## Slide 19
RACE: routing and auxiliary training
Backup: matched single-cycle comparison, seed 1219
19
Change from FSDR | Δ Test IoU (pp) | Image-paired 95% CI
Auxiliary training only | +0.1915 | [−0.0498, +0.4340]
Routing with auxiliary fixed | +0.2472 | [−0.0348, +0.5211]
Complete RACE | +0.4387 | [+0.1405, +0.7276]
Routing has a positive point estimate, but its interval crosses zero.
Single seed. These intervals describe image-level uncertainty.
The three-seed main study evaluates complete RACE as one module.
Notes: English speaker script
This earlier single-cycle study uses seed 1219 and the matched auxiliary-only control. It separates the routing increment from auxiliary training. The route alone has a positive point estimate but an image-paired confidence interval that crosses zero. The repeated three-seed study evaluates the complete module. We do not assign its entire gain to routing.
中文讲稿
该单周期实验使用 seed1219 及匹配的仅辅助监督对照，用来分离路由增量。路由点估计为正，但逐图配对置信区间跨零。三种子主实验评价完整模块，不能把全部增益归因于路由。
Sources (snapshot: 22 September 2026)
Source: previous defence slide 10, original evidence notes follow.
English speaker script
The completed auxiliary-only control helps separate the two changes. Adding auxiliary objectives produces a Test IoU point estimate of plus 0.1915 percentage points. Enabling routing with those objectives held fixed adds 0.2472 points. Both image-paired confidence intervals cross zero. The complete configuration improves by 0.4387 points, with an interval from 0.1405 to 0.7276 points. This supports improvement of the full configuration on this split and seed. It does not establish that the route alone has a reliable positive effect, and the additive arithmetic is not a proof of independent causal contributions.
中文讲稿
已经完成的仅辅助监督对照将两项变化分开：辅助目标的 Test IoU 点估计为 +0.1915 个百分点，固定辅助目标再开启路由为 +0.2472 个百分点。两者图像配对区间均跨零。完整配置的增益为 +0.4387 个百分点，区间为 [+0.1405,+0.7276]。因此支持该划分和种子上的完整配置改善，但路由独立贡献的证据还不充分，不能把全部提升归因于路由。
Evidence details
10,000 paired-image bootstrap resamples; RNG seed 20260914. These are not patient-cluster or across-training-seed intervals.
Sources · 15 September 2026
outputs/p8_binding_aux_20260915/FINAL_RESULTS.json
outputs/p8_research_20260914/test_20260915/TEST_RESULTS.json
outputs/p8_research_20260914/FINAL_PAIR_REPORT.md

## Slide 20
Validation and Test under the single-cycle recipe
Backup: three-seed means
20
Configuration | Val IoU (%) | Test IoU (%)
LViT-PLAM | 72.3228 ± 0.0550 | 75.4775 ± 0.0851
FSDR only | 72.7873 ± 0.2260 | 75.9833 ± 0.1511
PLAM + complete RACE | 72.5443 ± 0.0694 | 75.6962 ± 0.1068
FSDR + complete RACE | 72.9832 ± 0.2229 | 76.2262 ± 0.0456
Validation chooses the checkpoint. Test supplies the final reported result.
Mean ± sample SD across the same three seeds.
The result applies to the current split and shared training recipe.
Notes: English speaker script
The combined model has the highest validation and Test means among the four matched configurations. Validation IoU selects checkpoints. The headline result is Test IoU. The standard deviations describe variation across three training seeds, and the data-split limitations still apply.
中文讲稿
组合在四组匹配配置中具有最高验证和测试均值。验证 IoU 负责选权重，最终成绩以测试 IoU 为准。标准差表示三个训练种子之间的变化，数据划分限制仍然适用。
Sources (snapshot: 22 September 2026)
docs/results/stage1_overall_20260915/FINAL_REPORT.md
docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 21
Evaluation protocol
Split | Images | Role
Train | 5,716 | Parameter updates
Validation | 1,429 | Checkpoint selection and diagnosis
Test | 2,113 | Evaluation of selected checkpoints
224 × 224 inputs. Per-image macro IoU and Dice. Fixed probability > 0.5.
Val macro IoU selects Best. Test has prior research access.
Train/Val share 434 recoverable patient IDs. No recoverable Test overlap was found.
Anonymous cases prevent a claim of fully patient-independent splits.
Backup: evaluation protocol
21
Notes: English speaker script
The dataset has 5,716 training, 1,429 validation and 2,113 Test images. The primary study selects Best by validation macro IoU and evaluates that fixed checkpoint using probability strictly greater than 0.5. The patient audit finds 434 recoverable IDs shared by Train and Val. No recoverable Test ID overlaps Train or Val, but anonymous samples prevent proving full patient independence. The Test set has prior research access, so it is not an untouched prospective evaluation.
中文讲稿
数据划分为训练 5716、验证 1429、测试 2113。主实验由验证 macro IoU 选择 Best，再以严格 >0.5 的阈值评估该固定检查点。审计发现 Train/Val 共享 434 个可恢复患者 ID；可恢复 Test ID 未发现交叉，但匿名病例使完整患者独立性无法证明。Test 曾用于研究，不能宣称完全未接触的前瞻评估。
Sources (snapshot: 22 September 2026)
docs/results/plam_baseline_audit_20260916/AUDIT.md
docs/results/stage1_overall_20260915/FINAL_REPORT.md
docs/results/stage1_overall_20260915/FINAL_RESULTS.json

## Slide 22
Reproducibility of completed comparisons
Backup: implementation and result provenance
22
Evidence | Completed record
Primary module ablation | 4 configurations × 3 seeds, all Val and Test results
Matched training protocol | Single-cycle cosine, frozen text, no LoRA, 80 epochs
External methods | MMI-UNet, GuideDecoder and DD-CMD full Test outputs
Runtime provenance | Per-run source SHA, experiment tag and checkpoint hash
Integrated paper snapshot | FSDR + complete RACE source and archived result JSON
Archived runtime commits identify the experiments. Integration preserves their original provenance.
Notes: English speaker script
The repository integrates FSDR and complete RACE source with the result snapshots. Each experiment retains its original full source commit, tag and checkpoint hash. Integration did not retrain or re-evaluate models. The primary study contains 12 single-cycle models. External comparisons have their own source and recipe metadata. Reproduction follows those per-run records.
中文讲稿
仓库整合 FSDR 和完整 RACE 源码及结果快照。每项实验保留原始完整 SHA、标签和权重哈希，整合没有重新训练或推理。主实验为十二个单周期模型，外部对照有各自来源和配方。复现遵循每项运行记录。
Sources (snapshot: 22 September 2026)
docs/PAPER_RESULTS.md
docs/results/IMPORT_PROVENANCE.json
docs/results/stage1_overall_20260915/FINAL_REPORT.md
docs/results/stage1_overall_20260915/FINAL_RESULTS.json
docs/results/text_guided_baselines_20260920/FINAL_RESULTS.json

## Slide 23
Earlier RACE: report-target binding comparison
Configuration | Test IoU | Test Dice
FSDR control | 75.8098% | 84.4236%
RACE · original target binding | 75.9505% | 84.5237%
RACE · corrected target binding | 76.2485% | 84.7097%
Corrected vs original binding: Test IoU +0.2981 pp; image 95% CI [+0.0538, +0.5404].
Validation difference: −0.1107 pp (interval crosses zero).
Binding repair improves target assignment; it is not the architectural contribution.
Backup: binding comparison, seed 1219
23
Notes: Scope update (22 September 2026)
Historical comparison: seed 1219 only. This binding-repair diagnostic does not replace the complete-module three-seed ablation.
历史比较：仅 seed1219。绑定修复诊断不替代完整模块三种子消融。
English speaker script
Both RACE variants completed 80 epochs and used validation-selected checkpoints at epoch 75. Corrected binding improves Test IoU relative to original binding by 0.2981 percentage points, while the validation point estimate is lower by 0.1107 points and its interval crosses zero. We retain this split difference without retuning. The main contribution is the RACE mechanism. Repairing report-target assignment is implementation correctness and must not be presented as an additional architectural innovation. Both variants are reported so the correction is not hidden.
中文讲稿
两种 RACE 均完成 80 轮并使用 Val 选定的第 75 轮检查点。修正绑定相对原绑定的 Test IoU 增益为 0.2981 个百分点，而 Val 点估计低 0.1107 个百分点且区间跨零，两项结果同时保留，不据此回调参数。报告目标绑定修复属于实现正确性，不作为额外结构创新。
Sources · 15 September 2026
outputs/p8_binding_aux_20260915/FINAL_RESULTS.json
outputs/p8_research_20260914/test_20260915/TEST_RESULTS.json
outputs/p8_research_20260914/FINAL_PAIR_REPORT.md

## Slide 24
Paired-seed gains: full precision
Backup · Test macro IoU gain in percentage points · same-seed differences
24
Contrast | 1219 | 2027 | 3407 | Mean
FSDR − PLAM | +0.2423 | +0.6191 | +0.6561 | +0.5058
PLAM + RACE − PLAM | +0.2514 | +0.1790 | +0.2257 | +0.2187
Combined − FSDR | +0.4387 | +0.1704 | +0.1194 | +0.2428
Combined − PLAM + RACE | +0.4296 | +0.6104 | +0.5498 | +0.5300
Combined − PLAM | +0.6810 | +0.7895 | +0.7755 | +0.7487
Combined mean ± SD: IoU 76.2262 ± 0.0456% · Dice 84.7112 ± 0.0348%
All 12 individual runs, negative evidence and evaluation boundaries remain in the backup.
Notes: English speaker notes
These are the full-precision paired-seed comparisons behind the main chart. Each column subtracts two models with the same seed. Mean differences are computed before rounding. All five contrasts are positive in all three seeds.
中文讲稿
这是主图对应的完整精度配对比较。每列比较同一种子的两模型，先计算差值和均值再显示舍入值。五组对比、三个种子全部为正。
Sources
evidence/primary_results.json
Original: docs/results/stage1_overall_20260915/FINAL_RESULTS.json